## Slide 1
AI-Based Voice and Gesture Controlled Wheelchair
Smart mobility assistance
Gesture + voice control
ESP32 based prototype

## Slide 2
Problem Statement
Paralysis can cause severe loss of muscle movement
Patients may have limited control of their hands and arms
Independent wheelchair movement can become difficult
Continuous physical control may not be possible
Patients may depend on caregivers for mobility

## Slide 3
Proposed Solution
Hand gestures control
wheelchair movement
Voice commands provide
an alternative input
Python + MediaPipe
process gestures
Bluetooth sends commands to ESP32
hand gestures
voice commands
PROCESSING
python + mediapipe
COMMUNICATION
bluetooth
commands sent to ESP32
CONTROLLER
INPUT
ESP32

## Slide 4
System Architecture
User Input
Camera /
Microphone
AI Processing
Command
Generation
Bluetooth
Wireless
Transmission
ESP32
Microcontroller
L298N
Motor Driver
Motors
Wheel
Movement
MPU6050
Turning
Feedback

## Slide 5
Motor &
Turning Control
ESP32 controls two DC geared motors
L298N drives the motors
Differential drive produces turns
MPU6050 measures Z-axis rotation
90° and 180° turns are supported

## Slide 6
Working & Results
Hand gestures captured and recognized
Commands sent wirelessly via Bluetooth
ESP32 processes the received command
Motors respond to control the wheelchair
Prototype movement and turning achieved
Hand captured
by camera
Hand landmarks detected with MediaPipe
Command sent
via Bluetooth
Command received by ESP32
Motors respond
to command
Prototype movement and turning demonstrated

## Slide 7
Gesture & Voice Control
Stop
Turn Right
Turn Left
Move Backward
Voice Commands
Forward
Backward
Right
U-turn
Stop
Move Forward
Left

## Slide 8
Advantages & Future Scope
Contactless operation
Two control modes
Simple and
low-cost prototype
Wireless communication
Obstacle detection and emergency braking
GPS tracking, caregiver monitoring and autonomous navigation

## Slide 9
Thank You
AI-Based Voice and Gesture
Controlled Wheelchair
Questions & Answers